| Signs on the outside of the door indicate biosafety level, agent(s), and appropriate Personal Protective Equipment (PPE) for entry (e.g., BSL-2 sign, Toxic Chemicals in Use sign, Chemical Carcinogen sign, etc). |  |  |  |  |
| --- | --- | --- | --- | --- |
| Laboratory Emergency Information card is up-to-date and posted outside of the laboratory (e.g., yellow door card). |  |  |  |  |
| PPE is readily available to anyone entering the lab. PPE is properly worn by everyone working in the lab (add comment if necessary). |  |  |  |  |
| PPE is removed before exiting the laboratory. |  |  |  |  |
| The biological safety cabinet (BSC) has been certified within the past year. |  |  |  |  |
| The BSC is kept free of clutter and the front grate is kept clear. |  |  |  |  |
| The BSC vacuum lines are protected with liquid trap and in-line High Efficiency Particulate Air (HEPA) filters, as per http://www.cdc.gov/ biosafety/publications/bmbl5/index.htm, Section IV (pg 49), BSL-2 requirements. |  |  |  |  |
| The chemical fume hood has been certified within the past year. |  |  |  |  |
| The chemical fume hood is kept free of clutter. |  |  |  |  |
| Sharps are not left out; needles are never recapped (unless the one-handed method is used). |  |  |  |  |
| All sharps are disposed of properly. Sharps containers are disposed of when they reach ~2/3 – 3/4 full. See the UW Office of Biological Safety (OBS) website at www.biosafety.wisc.edu & then Resources/Waste Disposal. |  |  |  |  |
| Biohazard receptacles/containers are decontaminated/disposed of appropriately & "OK to Trash" stickers are used properly (if applicable). |  |  |  |  |
| All equipment used for biohazardous materials (e.g., freezers used for human cell line storage, liquid nitrogen cryogenic storage containers, incubators, etc.) properly labeled with "biohazard" stickers. |  |  |  |  |
| As applicable, all personnel that fill liquid nitrogen storage containers have been properly trained and the main cylinders are stored in an open area. |  |  |  |  |
| An autoclave is available for use by members of the lab. Please comment if your biowaste is disinfected by a central facility. |  |  |  |  |
| Autoclave is tested with biological spore strips/vials (efficacy testing) on a monthly basis. |  |  |  |  |
| Laboratory clutter is minimized. |  |  |  |  |
| Storage of cardboard is minimized, particularly on the floor (vermin control) &/or close to the ceiling (minimize fire hazards). |  |  |  |  |
| All surfaces and furniture in the lab have impermeable surfaces. |  |  |  |  |
| Food and drink is never kept or consumed in the lab. |  |  |  |  |
| Controlled substances (as per Drug Enforcement Administration, "DEA") are stored in a secure location. |  |  |  |  |
| Any potential aerosol generating activity is conducted in containment (e.g. BSC, sealed centrifuge rotors/cups). |  |  |  |  |
| Laboratory has a Chemical Hygiene Plan (see Laboratory Safety Guide – Appendix C, www.fpm.wisc.edu/chemsafety). |  |  |  |  |
| MSDSs are available for all chemicals present in the laboratory. |  |  |  |  |
| All work with volatile chemicals is conducted in a fume hood or ducted BSC. |  |  |  |  |
| Chemicals are properly stored (e.g., below shoulder height for large volume liquids, flammables away from corrosives, organics away from oxidizers, acids away from bases). |  |  |  |  |
| All containers in the lab (chemicals, reagents, water, disinfectants, etc.) are labeled. |  |  |  |  |
| Spill/exposure/release cleanup procedures are in place (see www.biosafety.wisc.edu -- Emergency Response tab/ Exposure & Spill Procedures). |  |  |  |  |
| A biological spill kit and a chemical spill kit is available and readily accessible (see www.biosafety.wisc.edu -- Emergency Response tab/ Exposure & Spill Procedures). |  |  |  |  |
| All personnel are familiar with the First Report of Biological Exposure or Release Event form at www.biosafety.wisc.edu. |  |  |  |  |
| Hand washing supplies are readily available within the lab (i.e. sink, soap, towels, trash can). |  |  |  |  |
| Gas cylinders are properly stored and secured. |  |  |  |  |
| Transport of hazardous materials between rooms and buildings is conducted in an appropriate manner (e.g. secondary containment, appropriately labeled). |  |  |  |  |
| Plumbed emergency shower is available and unobstructed (sign for emergency shower is clearly visible). |  |  |  |  |
| Plumbed emergency eyewash is available and unobstructed (sign for eyewash is clearly visible). |  |  |  |  |
| Eyewash is flushed weekly and documented. |  |  |  |  |
| Exits and corridors free from obstructions (i.e., lab aisle space are open at least 36-inches and hallways/corridors are open at least 44-inches for traffic). |  |  |  |  |
| Doors are kept closed in order to maintain proper room pressure (even for BSL-1 work). |  |  |  |  |
| All work conducted in your lab is covered in a current/approved biosafety protocol. |  |  |  |  |
| The Biosafety Protocol is up-to-date (i.e., all grants, personnel, equipment, agents, procedures, etc). Add a comment if an amendment is needed for any changes. |  |  |  |  |
| The Biosafety Protocol lists all rooms that are being used for your study (e.g., room location of BSC, of autoclave, etc). |  |  |  |  |
| The Biosafety Protocol is easily accessible and all personnel working in the lab are familiar with its contents. |  |  |  |  |
| All personnel listed in the biosafety protocol have undergone the 3 mandatory biosafety training modules at Learn@UW [e.g., currently required courses include (1) Biosafety 101-Risk Assessment, (2) Biosafety 104-Safe use of sharps, & (3) Biosafety 201-NIH guidelines]. |  |  |  |  |
| If applicable, all laboratory personnel receive annual Bloodborne Pathogen training (i.e., labs using primary or established human cell lines or tissues). |  |  |  |  |
| Do you have any specific questions or training needs that we can assist you with? Please add a comment if applicable. |  |  |  |  |