Laser Classification and Requirements

| Classification | Logotype | Warning Label Text | Outline of risk assessment |
| --- | --- | --- | --- |
| Class I | None Required Max Power <,= 0.39 mW | None Required | Levels of laser radiation are not considered to be hazardous. |
| Class IIa | None Required (Exposures < 1,000 s) Max power > 0.39 to 1.0 mW | None Required | Levels of laser radiation are not considered to be hazardous if viewed for any period of time less than or equal to 1 x 103 seconds. |
| Class II | CAUTION Max Power <,= 1 mW | Laser Radiation - Do not stare into beam | Levels of laser radiation are considered to be a chronic viewing hazard. |
| Class IIIa | CAUTION (Irradiance < 2.5 mW/cm2 Max power <,= 5 CAUTION (Irradiance >,= 2.5 mW/cm2) Direct Eye Exposure | Laser Radiation - Do Not Stare into Beam or View Directly with Optical Instruments Laser Radiation – Avoid Direct Eye Exposure | Levels of laser radiation are considered to be, depending upon the irradiance, either an acute intra beam viewing hazard or chronic viewing hazard, and an acute viewing hazard if viewed directly with optical instruments. |
| Class IIIb | DANGER Max Power <,= 500 mW | Laser Radiation – Avoid Direct Exposure to beam | Levels of laser radiation are considered to be an acute hazard to the skin and eyes from direct radiation. |
| Class IV | DANGER Max Power > 500 mW | Laser Radiation – Avoid Eye or Skin Exposure to Beam | Levels of laser radiation are considered to be an acute hazard to the skin and eyes from direct and scattered radiation. |